## Slide 1
EMBODIED AI · WEEK 23
Experiment 2: Teaching It To Balance
The same robot, the same test — but now something learns
Last week the hand-tuned controller fell over at 0.20 m/s and no setting could fix it.
This week I train a policy and put it through the identical test.
Shaoqin Li · Prof. Yi Sun · CCNY

## Slide 2
Where I left off
Experiment 1, in one sentence: a controller with two dials can hold the robot up, and nothing more.
▶ Experiment 1 — the hand-tuned controller, going down
WHAT I COULD NOT FIX
It survived a 0.20 m/s shove
from nobody. Not one of the
49 settings.
Because the controller only knows
one instruction — get back to the
pose I was told to hold.
Recovering from a shove means
choosing a DIFFERENT pose.
Stepping. Bending. Shifting weight.
Two dials cannot decide that.
So this week: can a neural network decide it? And can I prove the comparison is fair?

## Slide 3
The ten steps
Three are about setting the problem up. Four are training. Three are measuring — and the measuring is where the care goes.
1
Turn walking into standing
reuse the environment, zero the command
2
Decide what it can see
45 numbers in, 12 out
3
Write the reward
say what good means, without saying how
4
Train it
4 environments, 3M steps, 49 minutes
5
Read the curve
and the one number that looks like a bug
6
Design the test
copy Experiment 1's protocol exactly
7
Does it stand?
20 episodes, no disturbance
8
What is it paid for?
answer the obvious criticism
9
Push it
the same shove that beat the PD controller
10
Compare
against the number I had to beat
grey = set up the problem teal = train it sand = measure it

## Slide 4
STEP 1 / 10
Turn walking into standing
reuse the environment, zero the command
I did not write a new environment. I already had a walking task — standing is that task with the command set to zero.
WHAT I CHANGED
one flag: --fixed-cmd 0 0 0
go nowhere forward
go nowhere sideways
do not turn
WHY THAT IS THE RIGHT MOVE
The reward, the physics and the
observations stay byte-identical to
every other experiment.
So when I compare results later,
the difference is caused by the
policy — not by me quietly
changing the setup.
And there is a free bonus in it
The reward already contains a term that says “match the commanded velocity”. Set the command to zero and that term now means
“hold still on purpose”. I did not have to invent a single new reward term to turn a walking task into a standing one.

## Slide 5
STEP 2 / 10
Decide what it can see
45 numbers in, 12 out
The policy gets 45 numbers and produces 12. That is the entire interface.
IN — 45 numbers
3
how fast the body is rotating
3
which way is down, from the robot's view
3
what I am asking for — all zeros today
12
where each leg joint is
12
how fast each leg joint is moving
12
what it did on the last step
OUT
12 leg joint targets
a new pose, 50 times a second
THIS IS THE WHOLE DIFFERENCE
The PD controller had one pose,
fixed, forever.
This one picks a new target every
20 milliseconds — so it CAN decide
to crouch, or shift its weight.
Whether it learns to is the
experiment.

## Slide 6
STEP 3 / 10
Write the reward
say what good means, without saying how
The reward is how I say “good” without saying how. Fourteen terms — three of them do nearly all the work.
+1.5
match the commanded velocity
command is zero, so: hold still
+0.5
match the commanded turn rate
do not spin
+0.15
still standing
a small bonus each step
-5.0
stay upright
penalty for tilting
-10.0
hold your hip height
penalty for sinking
small
do not waste effort
penalty on torque
THE TRAP
The moment I put a “still
standing” bonus in there,
I invited one criticism:
“your robot didn't
learn to balance —
it learned to collect
the bonus.”
That is a fair objection,
and no training curve
can answer it.
I answer it in Step 8.

## Slide 7
STEP 4 / 10
Train it
4 environments, 3M steps, 49 minutes
Then I trained it — on the same laptop, with no GPU.
THE SETUP
PPO
4 environments
3,000,000 steps
49 minutes
0 GPUs
Randomisation is ON while
training — friction, mass,
motor gains, and a random
shove every few seconds.
It is being bullied on
purpose, so it learns
something robust.

## Slide 8
STEP 5 / 10
Read the curve
and the one number that looks like a bug
The real training log — all 60 checkpoints, nothing smoothed.
The thing that looks like a bug: episode length ends at 676 against a cap of 1000.
Read literally, that says it still falls a third of the time. It does not — randomisation and random shoves are ON during training and OFF during the test.

## Slide 9
STEP 6 / 10
Design the test
copy Experiment 1's protocol exactly
Before looking at any result, I decided how to test it — and copied Experiment 1's protocol exactly.
Randomisation
turned OFF
so the only disturbance is the one I inject
Push protocol
identical to Exp 1
same impulse, same moment, same magnitudes
Episodes
20 undisturbed, 5 per push
one run proves nothing
Checkpoint
best, not last
chosen on training reward — I say so openly
Metrics
three, not one
survival, tilt, and the reward breakdown
The second row is the one that matters.
If I had invented a nicer test for my own policy, the comparison to 0.15 m/s would be worthless. Same robot, same shove, same measurement.

## Slide 10
STEP 7 / 10
Does it stand?
20 episodes, no disturbance
First question: does it actually stand?
▶ 8 s, undisturbed — it barely moves
20 of 20 episodes reached the full 20 seconds. Maximum tilt across all of them: 3.22 degrees.

## Slide 11
STEP 8 / 10
What is it paid for?
answer the obvious criticism
Second question — the one I set up back in Step 3. Is it just collecting the survival bonus?
THE ANSWER
6.9%
of the score comes from
the survival bonus.
91% comes from velocity
tracking — from holding
still ON PURPOSE, which
is the actual task.
If it were gaming the
bonus, these would be
the other way round.
I raised this objection myself, before showing the result. That is the difference between a demo and an experiment.

## Slide 12
STEP 9 / 10
Push it
the same shove that beat the PD controller
Third question: the same shove that beat the hand-tuned controller.
▶ 0.30 m/s — it stays up
▶ 0.40 m/s — down in 2.2 s
Survives 0.30 m/s, five times out of five. Falls at 0.40. The hand-tuned controller survived 0.15.

## Slide 13
STEP 10 / 10
Compare
against the number I had to beat
Same robot. Same shove. Same measurement. The only thing that changed is what decides the pose.
EXPERIMENT 1 — two dials
0.15 m/s
survives
falls at 0.20
and no setting of the two dials
changes that
EXPERIMENT 2 — a trained policy
0.30 m/s
survives
falls at 0.40
twice the disturbance, on a test
I did not get to design
Learning roughly doubled it — and the reason is structural, not incremental.
The PD controller restores one fixed pose. The policy chooses a new pose fifty times a second — so it can crouch, or shift its weight,
or do whatever the shove requires. That is a different kind of thing, not a better-tuned version of the same thing.

## Slide 14
What I found
✓
Learning beats hand tuning, measurably
0.30 vs 0.15 m/s on an identical test
✓
It is not gaming the reward
the survival bonus is 6.9% of the score; velocity tracking is 91%
✓
A training curve cannot tell you it worked
reward went up — that says nothing about standing, steadiness or shoves
✓
The comparison is the hard part, not the training
copying Experiment 1's protocol is what makes the number mean anything
✓
Still only a simulator
whether this transfers to hardware is a question I have not answered yet
Every number came off my own screen, in the order you just saw it.

## Slide 15
What comes next — experiments 3 to 6
All four are already run — these are the real results, not a plan. I will take one per week from here.
3
What does learning cost?
Starting from a policy I already have, instead of from nothing, is at least 16× cheaper.
4
Which senses does it need?
I corrupt one sensor at a time. Gravity is the only one it cannot do without.
5
Why is a real robot harder?
I add control delay. Standing survives 80 ms; walking dies at 40.
6
Does the simulator lie?
Same policy, two physics models — then measure how far apart they drift.

## Slide 16
EXPERIMENT 3
What does learning COST?
I trained the same walking task twice — identical environment, reward, seeds and step budget. The only difference: one started from a policy I already had, the other from nothing.
▶ from scratch — down in 2.1 s
▶ warm start — still going at 5 s
Same number of training steps. Same everything else.

## Slide 17
EXPERIMENT 3
What the numbers say
1
At least 16× cheaper
the warm-started run at 50,000 steps is already past where the from-scratch run ended at 800,000
2
Well clear of the noise
the gap is 3.6 to 11.6 pooled standard deviations, across 15 runs per side
3
But the advantage shrinks
4.5× ahead early, 2.3× by the end — a head start, not a higher ceiling
Full walkthrough of Experiment 3 in a coming week.

## Slide 18
EXPERIMENT 4
Which senses does it actually need?
I froze the standing policy and corrupted one sensor at a time — dosing the noise in multiples of the noise that channel already saw during training.
▶ all senses intact
▶ gravity sense corrupted — down in 2.4 s
Same policy, same weights. Only the incoming sensor data changed.

## Slide 19
EXPERIMENT 4
What the numbers say
1
Gravity is the one it cannot lose
the only channel that breaks below 20× — it is the sole absolute reference for which way is up
2
Everything else is remarkably tough
joint angles, joint speeds and rotation rate all survive 10× their training noise
3
So sensing is not the weak link
which matters, because it points the sim-to-real problem at the physics instead
Full walkthrough of Experiment 4 in a coming week.

## Slide 20
EXPERIMENT 5
Why is a real robot harder than a simulator?
A real robot never acts on fresh information — there is always a delay. So I injected a fixed delay into a frozen policy and raised it until the robot fell.
▶ no delay — holds
▶ 160 ms of delay — down in 3.8 s
Identical policy. The only change is how stale its information is.

## Slide 21
EXPERIMENT 5
What the numbers say
1
Standing tolerates 80 ms; walking dies at 40
a 4× difference between two policies on the same robot
2
Because walking is a moving target
standing holds one pose; walking has to hit the right phase, and delay shifts phase
3
This is my best proxy for real hardware
the network round-trip on the real robot is worth roughly 40 ms
Full walkthrough of Experiment 5 in a coming week.

## Slide 22
EXPERIMENT 6
Does the simulator lie?
I took one frozen policy and ran it in two different physics models from an identical starting state — then measured how far apart they ended up.
▶ physics model A
▶ physics model B
Same weights, same start, same commands. Camera fixed so you can see them drift apart.

## Slide 23
EXPERIMENT 6
What the numbers say
1
The models disagree by a fixed amount
with the policy switched off, the difference doubles every 0.5–0.7 seconds
2
Feedback contains it — but not equally
standing holds the drift to 0.009 rad; walking only to 0.102 — about 10× worse
3
And walking's small error accumulates
after 20 seconds the two simulations are 2.8 metres and 58 degrees apart, with neither having fallen
Full walkthrough of Experiment 6 in a coming week.

## Slide 24
Where this is going
Two experiments down. Each one exists to make the next one measurable.
Exp 1
gave me a number to beat
0.20 m/s
Exp 2
beat it, on the same test
0.40 m/s
Exp 3–6
ask what it costs, what it needs,
and where the simulation stops being true
Questions