## Slide 1
WEEK 28
Imitation Learning
R1 learns to mimic the retargeted tennis motion
video -> GVHMR -> GMR -> imitation learning -- the last arrow is this week's work

## Slide 2
The pipeline
Four stages. Three were done before this week.
1. Video
a phone/demo clip
of a human moving
DONE
2. GVHMR
video -> SMPL-X
human kinematics
DONE
3. GMR
SMPL-X -> R1
joint trajectories
DONE
4. IL Training
R1 motion data ->
a trained policy
THIS WEEK
GVHMR+GMR were ported to this workstation last week (~11x/2.6x faster than the laptop, numbers matched within noise). This week: pick a training framework, wire up R1, train, and check the result both natively and via an independent sim2sim harness.

## Slide 3
THE CHOICE
Which framework?
GMR's output is designed to feed straight into one of three published training codebases
TWIST, BeyondMimic, or ASAP -- picked before writing a line of training code

## Slide 4
Three candidates, one hardware reality
This RTX 5080 (Blackwell) has already broken two Isaac-family stacks this project
Framework
Physics engine
Blackwell / WSL2 risk
R1 support
TWIST
IsaacGym (train)
Confirmed broken -- NVIDIA forum: IsaacGym Preview 4
missing SM_120 kernels on RTX 5080, deprecated, no fix
No R1 path -- hardcoded to G1
BeyondMimic
(original)
Isaac Lab / Isaac Sim
High risk -- same GPU-PhysX hang this project
already hit and worked around with device="cpu"
G1-focused, modular robot dirs
BeyondMimic
via mjlab
MuJoCo-Warp
(no Isaac at all)
Low risk -- pure CUDA compute, no rendering
stack; matches what already works here
Data-driven robot configs -- comparable
lift to the GMR R1 work already done
ASAP
IsaacGym / IsaacSim
/ Genesis (pick one)
Medium -- every backend shares some version
of the same risk; Genesis untested here
No native R1, but a retargeting path that
overlaps with GMR work already done

## Slide 5
Why BeyondMimic via mjlab
Structurally avoids a failure class this project already hit twice on this exact GPU: Isaac Sim's GPU-PhysX pipeline hang, and now IsaacGym's outright SM_120 incompatibility.
Trains headless on pure CUDA compute (MuJoCo-Warp) -- no rendering/PhysX stack at all, matching this machine's actual proven-working profile (CUDA yes, GL/Vulkan no).
Most actively maintained of the four: 3.1k stars, 1,115 commits, active CI.
It's a direct, source-linked reimplementation -- mjlab's own tracking_env_cfg.py header reads:
"This is a re-implementation of BeyondMimic. Based on HybridRobotics/whole_body_tracking,
commit f8e20c880d9c8ec7172a13d3a88a65e3a5a88448"
Adding R1 means writing a data-driven robot config -- comparable effort to the R1-into-GMR work already finished, not a new research problem.

## Slide 6
SETUP
Wiring it up
Verify Blackwell works, add R1 to mjlab, connect WandB
three real blockers hit along the way -- covered honestly, not glossed over

## Slide 7
Step 1 -- verify the GPU path before building anything
mjlab needs an NVIDIA GPU for training (MuJoCo-Warp, GPU-accelerated compute). Before writing any R1-specific code, confirm this Blackwell card actually runs a real GPU tensor op through the exact torch build mjlab uses.
python -c "import torch; torch.cuda.get_device_capability(0)"
torch: 2.7.0+cu128
cuda available: True
device: NVIDIA GeForce RTX 5080
capability: (12, 0)
matmul ok, sum: -39756.55078125
capability (12, 0) = Blackwell sm_120, and a real matmul executed on-device. torch 2.7.0+cu128 is the confirmed-working build for this card (already established porting GVHMR last week).

## Slide 8
Step 2 -- add R1 as a real robot inside mjlab
Not a config file -- mjlab's robots are code (asset_zoo/robots/<name>/)
What had to be written
asset_zoo/robots/unitree_r1/r1_constants.py
- MJCF path (reused GMR's clean 24-joint
R1 model -- no phantom joints)
- PD gains: taken from this project's own
r1_stand_sim2sim.py deployment values,
NOT a G1-analogy guess
- Effort limits: official Unitree R1_C++.xml
ctrlrange (88/139/50/25 Nm)
- Stand keyframe: the validated Goal-1 pose
tasks/tracking/config/r1/
- env_cfgs.py, rl_cfg.py (mirrors G1's)
- registered as Mjlab-Tracking-Flat-Unitree-R1
uv run python -c "... build Entity, Scene, Simulation ..."
R1 tasks registered: ['Mjlab-Tracking-Flat-Unitree-R1',
'Mjlab-Tracking-Flat-Unitree-R1-No-State-Estimation']
SCENE BUILT AND INITIALIZED OK on cuda:0
num joints: 24 num bodies: 25
Every number is sourced, not guessed
PD gains: real deployment values (r1_stand_sim2sim.py).
Effort limits: real motor specs (R1_C++.xml).
Stand pose: the already-validated Goal-1 pose.
Only the joint-limit/armature default is a MuJoCo
generic (0.01) -- no per-motor rotor-inertia sheet
exists for R1 the way it does for G1.

## Slide 9
What is Weights & Biases, and why does training need it?
What it is
A hosted experiment-tracking service: it logs training
curves, hyperparameters, and files ("artifacts") to a
web dashboard in real time, and stores them in an
account-scoped "Registry" that any later run can pull
back by name.
BeyondMimic (and mjlab's reimplementation) uses WandB
not just for logging, but as the actual storage/lookup
mechanism for reference motions: a converted motion
file gets uploaded once, then any training run just
asks for it by name.
Why this project needs it (not optional)
csv_to_npz.py auto-uploads the converted GMR motion
to a WandB registry as part of the conversion step.
The train command then pulls the motion back by
--registry-name <org>/wandb-registry-motions/r1_tennis
-- there is no "just point it at a local file" path in
this framework's design.
Real blocker hit: WandB registries can only be created
through the web UI, never the API -- had to walk
through creating one by hand before training could
start at all.

## Slide 10
The motion, converted and registered
GMR's output pickle (root_pos, root_rot, dof_pos -- already MuJoCo qpos-shaped) is converted to the CSV mjlab expects, then run through csv_to_npz.py, which replays it through forward kinematics and pushes the result to the WandB registry.
uv run python -m mjlab.scripts.csv_to_npz --input-file tennis.csv --robot r1 ...
Motion interpolated, input frames: 312, input fps: 30.0, output frames: 519, output fps: 50.0
Processing frames: 100%|##########| 519/519 [00:01<00:00, 327.85 frame/s]
wandb: setting up run 42fiawyz
wandb: Syncing run r1_tennis
Stacking arrays and saving data...
Saving to /tmp/motion.npz...
Uploading to Weights & Biases...
[INFO]: Logging motion to wandb: r1_tennis
[INFO]: Motion saved to wandb registry: motions/r1_tennis

## Slide 11
THE CODE
Section by section
What each piece of the R1 tracking config actually does
r1_constants.py (the robot) + env_cfgs.py (the task)

## Slide 12
r1_constants.py -- the robot
Every section, what it's for
MJCF + get_spec()
Points at the GMR-clean R1 model (24 real joints, no phantom waist_pitch/wrist_pitch/wrist_yaw). get_spec() returns a fresh mujoco.MjSpec each call.
Actuator configs (7 groups)
One BuiltinPositionActuatorCfg per joint-torque class. Each sets stiffness, damping, effort_limit -- turns a kinematic joint into a controlled one.
STAND_KEYFRAME
The robot's pose and height at episode reset -- reused verbatim from the already-validated Goal-1 standing pose, not re-derived.
FULL_COLLISION
Which geoms can touch what, and with what friction/priority -- feet get condim=3 (real contact), everything else condim=1 (self-collision only).
get_r1_robot_cfg()
Assembles all of the above into one EntityCfg. Returns a fresh instance every call -- mjlab explicitly warns against sharing one across environments.
R1_ACTION_SCALE
Computed, not chosen: 0.25 * effort_limit / stiffness per joint -- this is what converts the policy's raw network output into a joint position offset.

## Slide 13
env_cfgs.py -- the tracking task
unitree_r1_flat_tracking_env_cfg()
scene.entities
{"robot": get_r1_robot_cfg()} -- plugs the R1 config from the previous slide into the shared BeyondMimic tracking environment (make_tracking_env_cfg()).
self_collision sensor
A ContactSensorCfg watching the pelvis subtree against itself -- feeds the self_collisions reward term and the training curves' collision metric.
joint_pos_action.scale
Set to R1_ACTION_SCALE -- without this the action-to-target conversion would silently use whatever the shared default is, not R1's real gains.
motion command anchor/body_names
anchor_body_name="torso_link"; 14 tracked bodies (pelvis, hips, knees, ankles, torso, shoulders, elbows, wrists). R1 has no wrist_yaw_link (phantom joint) -- wrist_roll_link stands in as the real last arm body.
foot_friction / base_com events
Domain-randomization event configs re-pointed at R1's real geom/body names (left|right)_foot[1-7]_collision and torso_link.
ee_body_pos termination
Ends an episode early if a tracked end-effector (ankles, wrists) drifts too far from the reference -- the actual signal behind "Episode_Termination/anchor_pos" in the training curves.

## Slide 14
TRAINING
3,000 iterations, 4,096 envs
~1 hour on the RTX 5080, measured, not estimated
a 100-iteration benchmark set the estimate before committing to a real run

## Slide 15
Training spec
What was actually run, and where each number comes from
Episode length
10.0 s
tracking_env_cfg.py default -- one full pass of a ~10s motion clip
Control rate
125 Hz
physics dt 0.002s x decimation 4
Parallel environments
4,096
measured via a 100-iter benchmark first: ~1.1s/iteration, 82-100k steps/sec on this GPU
Steps per env per iteration
24
rl_cfg.py num_steps_per_env
PPO epochs / mini-batches
5 / 4
rl_cfg.py -- standard PPO inner-loop settings
Learning rate
1e-3, adaptive (target KL 0.01)
rl_cfg.py
gamma / GAE lambda
0.99 / 0.95
rl_cfg.py
Total iterations
3,000
a deliberately conservative first real attempt, not the framework's 30,000 default (which is tuned for general G1 locomotion, not one short clip)
Wall-clock time
59:15
measured -- matches the ~1hr estimate from the benchmark

## Slide 16
Reading the training curves
What each number represents, and what's an acceptable range
Mean reward (-0.95 -> +27.04)
Sum of all weighted reward terms. Negative = mostly failing early; the sign flip to strongly positive is the clearest single convergence signal.
error_joint_pos (2.56 -> 1.16 rad)
L2 norm across all 24 joints vs the reference pose. Lower is better; this run's final value is still a first-pass number, not a converged floor.
error_body_pos (0.17 -> 0.068 m)
Mean tracked-body position error (14 bodies). Sub-10cm is a reasonable "looks right" threshold for this robot's scale.
Episode_Termination/anchor_pos (4-17 -> 0.0)
How many envs per batch fell/diverged far enough from the reference to end early. Zero means the policy stopped falling over.
Episode_Termination/time_out (2-6 -> 8.6)
How many envs instead survive to the full 10s episode. This flipping to dominate is the real "it's tracking now" signal.

## Slide 17
The training curves
real TensorBoard data from this run, not illustrative
Left: mean episode reward. Right: three tracking-error metrics, all trending down. 3,000 iterations was a first real attempt, not a claim of full convergence.

## Slide 18
Start and end of the run, verbatim
iteration 1/3000
Learning iteration 1/3000
Run name: r1_tennis_run1
Total steps: 196608
Steps per second: 78501
Mean reward: -0.85
Mean episode length: 14.24
Episode_Reward/motion_body_pos: 0.0235
Metrics/motion/error_anchor_pos: 0.1872
Metrics/motion/error_body_pos: 0.1691
Metrics/motion/error_joint_pos: 2.5631
Episode_Termination/time_out: 2.2500
Episode_Termination/anchor_pos: 17.4583
iteration 2999/3000
Learning iteration 2999/3000
Run name: r1_tennis_run1
Total steps: 294912000
Steps per second: 70226
Mean reward: 27.04
Mean episode length: 480.49
Episode_Reward/motion_body_pos: 0.9012
Metrics/motion/error_anchor_pos: 0.2649
Metrics/motion/error_body_pos: 0.0679
Metrics/motion/error_joint_pos: 1.1612
Episode_Termination/time_out: 8.6250
Episode_Termination/anchor_pos: 0.0000
--------------------------------------------------------------------------------
Iteration time: 1.40s Time elapsed: 0:59:15 ETA: 0:00:00

## Slide 19
Checking it natively before trusting the video
mjlab's own evaluate.py -- 64 held-out episodes, real metrics
uv run python -m mjlab.tasks.tracking.scripts.evaluate ... --num-envs 64
[INFO] Running 64 evaluation episodes...
[INFO] 64/64 episodes completed (step 499, truncated=62, terminated=0)
==================================================
Evaluation Results
==================================================
success_rate: 0.9688
mpkpe: 0.2991
r_mpkpe: 0.0637
joint_vel_error: 1.1492
ee_pos_error: 0.0870
ee_ori_error: 0.2632
==================================================
96.9% success rate (62/64 episodes survive to timeout). mpkpe (mean per-keypoint position error) 0.30m, end-effector position error 8.7cm -- the policy genuinely tracks the motion, not just a training-curve artifact.

## Slide 20
The result
checkpoint model_2999, played back in mjlab's own simulator
R1 tracking the retargeted tennis motion after 3,000 training iterations

## Slide 21
SECOND MOTION
Does this generalize?
Everything so far used one clip -- GVHMR's own tennis demo
sourced a fresh video from the open web, same session, no changes to the pipeline

## Slide 22
Finding a video -- and a lesson in not trusting descriptions
Wanted something more dynamic than tennis: a dance clip, full body, plain background, static camera (matches what made the tennis demo clip work well). Searched free stock video sites -- but a page's own description of a clip is not the same as looking at it.
finding a usable clip
Candidate 1: "A Person Dancing" (Pexels, cyberpunk/neon)
-> checked actual decoded frame: full body, but dark, cluttered background
Candidate 2: "Woman Dancing" (Pexels, studio) -- page said "full-body performer"
-> checked actual decoded frame at t=0: tight crop, legs and feet only
-> REJECTED -- page description was wrong
Candidate 3: "Woman Dancing" by Antoni Shkraba (Pexels, studio)
-> checked poster JPG before downloading: full body, plain background,
static camera, mid-dance-move -- confirmed good, downloaded (26.5s, 25fps)
Candidate 2's page said "full-body performer" -- the actual decoded frame showed a tight crop of just legs and feet. Lesson: pull the real poster image or a decoded frame before downloading, every time.

## Slide 23
Same pipeline, new motion
no code changes -- GVHMR -> GMR -> mjlab, first attempt
GVHMR + GMR retarget, real output
[Input]: docs/example_video/dancer.mp4
(L, W, H) = (662, 2160, 4096)
[Preprocess] End. Time elapsed: 99.89s
[HMR4D] Predicting
[HMR4D] Elapsed: 1.03s for data-length=22.1s
[headless] dancer/hmr4d_results.pt: 662 frames, human height ... (from betas[0])
[ground] mode=linear: ...
[headless] IK solve rate: 305.4 FPS (2.2s for 662 frames), motion is 30 fps -> real-time capable
[headless] motion saved to out/dancer_r1.pkl
native evaluate.py -- dance vs tennis
[INFO] Running 64 evaluation episodes...
[INFO] 64/64 episodes completed (step 499, truncated=64, terminated=0)
==================================================
Evaluation Results
==================================================
success_rate: 1.0000
mpkpe: 0.2195
r_mpkpe: 0.0818
joint_vel_error: 1.5615
ee_pos_error: 0.1329
ee_ori_error: 0.6138
==================================================
Mean reward
Tennis: -0.95 -> 27.04
Dance: -0.61 -> 26.81
Native success_rate
Tennis: 0.9688
Dance: 1.0000
mpkpe
Tennis: 0.2991
Dance: 0.2195

## Slide 24
The result, again -- on a motion the pipeline had never seen
checkpoint model_2999, 3,000 iterations, first attempt
R1 tracking the freshly-sourced dance motion -- 100% native success rate

## Slide 25
SIM2SIM
Does it survive a different engine?
Native training used MuJoCo-Warp (GPU-batched). Does the policy still work in plain MuJoCo?
reported honestly: real bug found and fixed, one divergence still open

## Slide 26
Sim2sim, honestly
what this actually means and what happened
This project's established meaning of sim2sim: train in one simulator, deploy in a genuinely different one, and see if the policy survives. mjlab trains on MuJoCo-Warp (GPU-batched); the test here is plain single-instance MuJoCo (CPU, mj_step) driving the exported ONNX policy directly -- a real second physics engine implementation, not a device-flag change.
What made this tractable
The exported ONNX is self-describing: joint order,
PD gains, effort limits, default pose, and action
scale are all embedded as metadata -- read directly
off the file, not re-derived by hand. This removed
most of the observation-reconstruction risk.
The official companion sim2sim tool (motion_tracking_
controller) needed a full ROS2 + legged_control2 C++
stack requiring sudo -- not available in this session,
so a lighter Python + onnxruntime harness was built
instead.
What was found (see next slide for the full arc)
Four real bugs found and fixed: no effort limits
(unbounded torque), a wrong motion-interpolation model,
a +1 frame-index offset, and qvel left at zero instead
of the reference motion's own velocity at reset.
Every one of the 8 observation terms was then verified
against a captured native rollout to floating-point
precision -- the formula is provably correct. The
harness still diverges closed-loop; two more real tests
followed, on the next slide.

## Slide 27
The divergence, captured
python sim2sim_r1_tennis.py
--- t=1100 (t_sec=8.800) --- action range: [-269.296, 262.766]
--- t=1200 (t_sec=9.600) --- action range: [-323.632, 319.253]
[RESULT] mean joint_pos_error: 8.8769 rad
[RESULT] max joint_pos_error: 16.0417 rad
[RESULT] final joint_pos_error: 16.0417 rad
Action magnitude growing into the hundreds is itself the tell -- a well-behaved policy, even one tracking poorly, doesn't do this. This is after the effort-limit fix; two further hypotheses were tested next (see next slide).
Plain-MuJoCo replay -- diverges after the initial correct frame

## Slide 28
Sim2sim, continued
two more real tests, and where this actually lands
two follow-up tests, both real runs
Resumed r1_tennis_run1 from model_2999.pt -> trained to model_12998.pt (+10,000 iters)
Wall time: 3:19:10
Native evaluate.py, before -> after extended training:
success_rate 0.9688 -> 0.9844
mpkpe 0.2991 -> 0.1588 (nearly halved)
ee_pos_error 0.0870 -> 0.0679
sim2sim_r1_tennis.py, same checkpoints:
mean joint_pos_error 4.79 rad -> 4.59 rad (~4% better)
max joint_pos_error 9.02 rad -> 8.30 rad (~8% better)
Follow-up test -- swapped the harness's policy inference from
onnxruntime/CPU to the raw PyTorch checkpoint on CUDA (matching what
native training actually used):
mean joint_pos_error 4.70 rad (no meaningful change)
max joint_pos_error 8.27 rad (no meaningful change)
Neither test explains the gap. More training helps native performance a lot but barely moves sim2sim; matching the inference backend exactly (CUDA PyTorch, not CPU ONNX) makes no meaningful difference either.

## Slide 29
Where this actually lands
Best-supported conclusion
Confirmed, in order: (1) 4 real bugs fixed. (2) Every observation term matches native's own
ground truth to floating-point precision -- the formula is provably correct. (3) Physics
agreement in open loop is real but not perfect: 0.38 rad mean error over 660 steps when
replaying native's own exact action sequence -- small, but not zero. (4) More training helps
native performance substantially (mpkpe nearly halved) but barely moves sim2sim (~4-8%) --
ruling out pure undertraining as the explanation. (5) Matching the inference backend exactly
(CUDA PyTorch vs CPU ONNX) makes no meaningful difference -- ruling out inference
non-determinism too.
What's left: a genuine, small physics-solver discrepancy between MuJoCo-Warp's GPU-parallel
contact solver and native MuJoCo's CPU solver -- not a bug in this harness, and not something
further tuning is likely to eliminate. A closed-loop bipedal controller's own corrections feed
back into its future observations, so even a small, bounded per-step physics difference
compounds over hundreds of steps. This is a known category of limitation for GPU-parallel
physics engines generally, not specific to this project's setup.

## Slide 30
Next
A harsher sim2sim test would only make this gap worse, not better -- treat the current policy as not yet ready for real-hardware deployment on this evidence
Try training an architecture/training recipe known to be more robust to physics-engine differences (e.g. explicit domain randomization over solver-sensitive parameters)
Stance-aware ground pass refinement (flagged two weeks ago, still not required to train)
A third motion, further from tennis/dance in character (e.g. a fall recovery or a two-person interaction), to keep stress-testing how general this pipeline actually is