## Slide 1: Baselines & OOD
chu

## Slide 2: Goal: comparison + better OOD
① Add newer baselines (v3)
② Better OOD model (v4)
RWM
2025
history world model
QWM-style
2026
conditioned on robot parameters
DeLaN-style
2025
energy structure + known PD
PETS-style
2018
probabilistic ensemble
Graph MLP
ours
per-finger graph, MLP mechanism
Which design makes the mass extrapolate?
2×2 test: how the mass enters × where forces come from
→ new model: mass-factorized Lagrangian (MFL)
train: light links
gap
test: heavy (≈1.85×)
CausalWorld TriFinger · 100-step forecast from s₃₂ (250 Hz)
same data and scoring for every model · 10 runs
Notes: 这次汇报的目的有两个，对应这两周做的两个 notebook。
① 补充对比实验（v3）。之前我们只和 RWM、PETS 比，PETS 是 2018 年的，太老；教授也指出对比不够突出。所以 v3 加入了更新的方法：QWM-style（2026，按机器人参数条件化的世界模型；作者没公开代码，我们把它的参数输入方式装在 RWM 主干上，所以叫 QWM-style）、DeLaN-style（Context-aware DeLaN 2025 的做法，能量结构 + 已知 PD 控制器），以及 Graph MLP。每个模型都有'给真实质量'和'不给质量'两个版本，数据、预测窗口、评分方式完全相同。
② 把更好的算法用在 OOD 问题上（v4）。v3 显示我们的 B 还不是最好的，所以 v4 不再只加基线，而是做受控比较，找出到底是哪个设计让模型能外推，再在此基础上提出新模型 MFL。
设定和之前一样：CausalWorld TriFinger，9 个活动连杆的质量训练时取轻的一段，测试时取重的一段，中间留空档，测试质量平均约为训练的 1.85 倍。所有模型从第 32 步的真实状态出发，用记录的动作往后预测 100 步（250 Hz，0.4 秒），只反馈自己的预测。2 个任务 × 5 个 seed = 10 组。

## Slide 3: v3: masses help only physics
Chart: 
| RWM | Graph MLP | PETS | QWM- style | DeLaN- style | Ours (B)
gain | -1.37 | -1.12 | -0.67 | -0.35 | 0.09 | 0.07
OOD R² with true masses − without · runs improved: 0/10 (red), 10/10 (blue)
Chart: 
| PETS | QWM- style | Ours (B) | Graph MLP | RWM-50 | DeLaN- style
R2 | 0.503 | 0.725 | 0.746 | 0.747 | 0.752 | 0.754
best version of each model, OOD R² (median of 10 runs)
Physics structure turns the true mass into a gain — but no model is clearly most accurate yet.
Notes: 左图：每个模型'给真实质量'减去'不给质量'的 OOD R²（重手指，100 步平均，10 组的中位数）。正数表示真实质量有帮助。
黑盒模型（RWM、PETS、Graph MLP、QWM-style）拿到比训练更重的质量反而变差，10 组里 0 组变好。RWM 从 0.72 掉到 −0.65。原因是网络只在轻质量上学过'质量怎么起作用'，超出范围后外推方向是错的。QWM-style 掉得最少（−0.35），但也是 0/10。
带物理结构的模型（DeLaN-style 和我们的 B）拿到真实质量后变好，10/10：DeLaN-style +0.094，B +0.071。
成对干预测试（两条仿真从同一状态、同一组动作出发，只改一个连杆质量）也一致：越界时第 1 步的效应分数 DeLaN-style 0.89、B 0.85，而 Graph MLP −0.21、PETS −0.18（符号都反了）。但到第 25 步，所有模型都接近 0，多步效应仍然是难点。
右图：每个家族最好版本的 OOD R²。最好的几个都在 0.75 左右：DeLaN-style 0.754、RWM-50（不给质量）0.752、B 0.746、Graph MLP（不给质量）0.747。所以结论是：物理结构让真实质量变成有用的信息，但还没有模型在准确率上明显领先。B 对 DeLaN-style 只赢 3/10。这就是 v4 要改进的地方。

## Slide 4: v4: which design extrapolates?
mass as network input
mass as coefficient
forces:
free network
forces:
from energy
conditioned net
current B
DeLaN-style
fused B
Proposed: MFL
fused B + three rules
P all inertia and potential ∝ known mass
K a link reads only its moving joints
S the three fingers share link modules
each rule removed once (ablation)
Fair: same known PD controller, residual, integrator, data and training · every cell has a fixed-mass control
Measured: OOD error vs distance beyond the training range · paired-simulation intervention response
Notes: v4 回答'收益到底来自哪里'。我们把模型拆成两个因素，各取两种做法，组成 2×2：
列：质量怎么进入模型——当成网络输入（网络自己学质量的作用），或者当成物理系数（惯性 = Σ 质量 × 学到的形状，质量翻倍惯性就翻倍）。
行：力从哪里来——网络自由输出科氏力和重力，或者由同一个动能和势能推导出来（拉格朗日结构）。
四格分别对应：参数条件化网络、我们现在的 B、DeLaN-style（直接复用 v3 的模型）、以及融合版 B。
公平性：四格用同一个已知 PD 控制器、同一个不读质量的残差、同一积分器、同一数据和训练配方；每一格都另外训练一个固定质量的对照，所以'给质量的收益'在每一格里都能单独算。
在融合版 B 基础上，我们提出 MFL，加三条规则：P，所有和质量有关的惯性和势能都乘以已知质量（没有不随质量变的部分）；K，每节连杆只受带动它的关节影响（运动链结构，FeLaN 也用类似结构，我们会引用）；S，三根手指共享连杆模块。每条规则都有去掉它的消融。
评价：OOD 预测误差、按越界程度分层的误差、成对仿真的干预响应，以及模型内部惯性是否随质量正比变化。
状态：notebook 已经做好并在合成数据上测试通过，正在跑真实数据。