## Slide 1: Week 14
chu

## Slide 2: Two kinds of shift
① A shortcut breaks
② The true cause leaves its range
mass
colour
next state
graph cuts the decoy
−64% error (our SCM, 50/50 seeds)
CausalWorld: 0.74 vs −0.20 without graph
mass
heavier than ever seen
next state
?
nothing to cut: the mechanism must extrapolate
This week

## Slide 3: Setup: heavier fingers at test
CausalWorld TriFinger (Ahmed et al., 2020)
Mass of each of the 9 moving links
train: light
gap
test: heavy
0%
40%
60%
100%
of each link's allowed range
masses, finger 1
joints, finger 1
masses, finger 2
joints, finger 2
masses, finger 3
joints, finger 3
a link mass acts only on its own finger (checked by intervention)

## Slide 4: Data: what each run uses
Learn on light fingers
  lower 40% of each link's mass range
Exam on heavy fingers
  upper 40%: 1.85× heavier, never seen
Ceiling: trained on heavy, reference only
Probe: change one mass, compare
10 runs: 2 tasks × 5 seeds
Chart: 
| learn (light) | check (light) | test (light) | EXAM (heavy) | ceiling (heavy) | probes
episodes | 864 | 96 | 240 | 300 | 1200 | 300
episodes per run (0.6 s each); blue = light fingers, red = heavy

## Slide 5: Idea: physics inside the MLP
Before: MLP
joints, action, mass → MLP → acceleration
how the mass acts: learned from
light fingers only
heavy finger → ?
Now: rigid-body layer
inertia(m) × acceleration = torque − gravity(m) + contact
inertia, gravity: linear in m (fixed by physics)
networks learn only the mass-free parts
heavy finger → the same law
robot dynamics are linear in the link masses (cf. DeLaN, Lutter et al., ICLR 2019)

## Slide 6: Result 1: physics layer wins
MLP + mass is worse than ignoring the mass
Rigid-body layer is best
  beats 'mass removed' in 9/10 runs (p = 0.004)
Formula search (EQL): unstable, dropped
Chart: 
| one MLP (no graph) | graph + MLP | graph, mass removed | graph + formula | graph + rigid-body
R2 | -0.61 | -0.27 | 0.39 | 0.41 | 0.48
joint R² on heavy fingers, mean over 50 steps, median of 10 runs

## Slide 7: …but the win was not the mass
Same layer, mass frozen at the training average
  just as good: 4/10 runs, p = 0.70
The win came from the layer's structure
The mass was not learned, even in range
Chart: 
| rigid-body (with mass) | rigid-body (mass frozen) | MLP, mass removed
R2 | 0.486 | 0.491 | 0.394
joint R² on heavy fingers, 25 Hz, median of 10 runs

## Slide 8: Why: 25 Hz cannot see the mass
The mass acts through acceleration
At 25 Hz the velocity change is unpredictable
Record every physics step: 250 Hz
  same system: 10 × 1/250 s = 1 × 0.04 s, identical
Chart: 
| MLP, mass removed | rigid-body (with mass)
25 Hz (every 0.04 s) | 0.029 | 0.069
250 Hz (every 0.004 s) | 0.725 | 0.756
R² of the one-step velocity change, light fingers, median of 10 runs

## Slide 9: Mass test: predict the change
same state
+ same action
link mass = m
link mass = m′
simulator, 1 step:
speed 1.000
simulator, 1 step:
speed 0.980
true change
= −0.020
model, same two questions | speed, mass m | speed, mass m′ | change | score
MLP | 0.998 | 0.996 | −0.002 | 0.19
rigid-body layer | 1.001 | 0.990 | −0.011 | 0.80
score = 1 − (model change − true change)² ÷ (true change)² 1 = exact change · 0 = predicts no change
round numbers for illustration; the real score sums over every pair and all 18 joint values (angle and speed of 9 joints)

## Slide 10: Result 2: MLP misses the change
Inside the training range
  MLP 0.19, rigid-body 0.77
Outside: heavier than ever seen
  MLP −0.14: worse than 'no change'
  rigid-body 0.81: no loss
  rigid ahead in 10/10 runs, p = 0.002
Why MLP misses it: mass moves one step ~2%
  ignoring it barely hurts ordinary accuracy
Chart: 
| new mass inside training range | new mass outside training range
MLP (mass as an input) | 0.19 | -0.14
rigid-body layer (mass in the formula) | 0.77 | 0.81
change score (previous slide), one step, median of 10 runs

## Slide 11: Result 3: not over 150 steps
With the mass: better for ~10 steps
  worse after 50
Trained on the next step only
  its errors are never fed back
→ train on rollouts (05e)
Chart: 
| 1 | 10 | 50 | 100 | 150
rigid-body (with mass) | 0.936 | 0.867 | 0.664 | 0.281 | -0.043
rigid-body (mass frozen) | 0.887 | 0.803 | 0.683 | 0.486 | 0.312
MLP, mass removed | 0.892 | 0.828 | 0.514 | 0.151 | -0.73
trained on heavy (ceiling) | 0.946 | 0.945 | 0.836 | 0.653 | 0.52
joint R² on heavy fingers at step k (250 Hz), median of 10 runs

## Slide 12: Rollout training: still a tie
Train on 50-step rollouts, not one step
  both models: 0.46–0.55 → 0.73
With the mass vs mass cut: 0.734 vs 0.733
  3/10 runs; 95% CI [−0.07, +0.01]
The mass helps only the first ~10 steps
Chart: 
| learned torque, WITH the mass | learned torque, mass CUT
next-step training | 0.46 | 0.55
rollout training | 0.73 | 0.73
joint R² on heavy fingers, mean over 150 steps, median of 10 runs

## Slide 13: Fix: write the motor rule in
acceleration = ( motor force + contact − gravity(m) ) ÷ inertia(m)
inertia and gravity grow in proportion to each link's mass: fixed by physics, never learned
A · motor force learned
a network guesses it from
target, angle, speed
B · CausalWorld's motor rule
10 × (target − angle) − damping × speed
capped at 0.36 N·m: nothing learned
each model also has a mass-cut twin: same model, always told the light average

## Slide 14: Result 4: now the mass matters
Motor rule written in (B)
  WITH the mass beats mass cut
  10/10 runs at every step
150-step mean 0.73 vs 0.61
  95% CI [+0.10, +0.14]
Light fingers: +0.01 only
  the mass pays off out of range
Chart: 
| 1 | 10 | 25 | 50 | 75 | 100 | 125 | 150
B, WITH the mass | 0.978 | 0.948 | 0.881 | 0.804 | 0.72 | 0.646 | 0.581 | 0.518
B, mass CUT | 0.868 | 0.865 | 0.609 | 0.638 | 0.605 | 0.541 | 0.53 | 0.439
joint R² on heavy fingers at step k, rollout-trained, median of 10 runs

## Slide 15: Result 5: best early, not late
First 25 steps: at the ceiling
  step 1: 0.98 vs 0.97
After ~40 steps: old best ahead
  step 150: 0.52 vs 0.65
150-step mean: 0.73 vs 0.73
  not yet the most accurate model
Chart: 
| 1 | 10 | 25 | 50 | 75 | 100 | 125 | 150
B, WITH the mass | 0.978 | 0.948 | 0.881 | 0.804 | 0.72 | 0.646 | 0.581 | 0.518
old best: A, mass cut | 0.877 | 0.848 | 0.702 | 0.819 | 0.744 | 0.742 | 0.677 | 0.655
ceiling: B trained on heavy | 0.972 | 0.966 | 0.902 | 0.864 | 0.815 | 0.746 | 0.711 | 0.652
joint R² on heavy fingers at step k, rollout-trained, median of 10 runs

## Slide 16: What holds, what does not
✓
250 Hz resolves the dynamics
velocity R² 0.03 → 0.73
✓
Mass change predicted, also out of range
score 0.81 vs MLP −0.14; 10/10
✓
No leakage; MLP fails on the unseen mass
audit: 10/10 runs
✓
Motor rule in → the mass matters out of range
+0.12, 10/10 at every step
✗
Most accurate on heavy fingers
best for 25 steps, behind after ~40
!
Base joint limited by the recorded state
best possible R² 0.58 (tip 0.98)

## Slide 17: Next: why it degrades late
① Diagnose
which part fails first;
how much small errors grow
② Whole episodes
train on 150-step rollouts:
steps 51–150 never trained
③ Learned correction
small, added to the motor rule;
never sees the mass
every fix keeps its mass-cut twin: the mass must still matter
then: robustness — shift size, one heavy finger, more seeds